## Slide 1: Weather-Aware Power Cast
ML project coordination dashboard
2021–2024 electricity-demand data
Notes: Source: Weather Aware Power Cast notebook supplied by the user. All reported model metrics come from its recorded validation and 2024 test evaluation.

## Slide 2: Model performance dashboard
Selected model
Linear regression
2024 test R²
0.9991
2024 test MAE
24.59 MW
Chart: Validation MAE by approach (MW)
| 1-day baseline | 5-min baseline | Linear | Random forest | XGBoost
MAE | 463.38 | 27.34 | 23.48 | 24.61 | 26.84
Notes: Validation results reported in the supplied notebook. The one-day persistence baseline is included as a long-horizon comparison. Lower MAE is better.

## Slide 3: 2024 test-set results
24.59 MW
Mean absolute error
41.87 MW
Root mean square error
Five-minute persistence MAE: 29.09 MW. The selected model reduced MAE by 15.5% on unseen 2024 data.
Chart: Five-minute test MAE (MW)
| Persistence baseline | Selected linear model
MAE | 29.09 | 24.59
Notes: Final test results and baseline comparison reported in the supplied notebook. The selected linear model was refit on training and validation data before the unseen 2024 evaluation.

## Slide 4: Forecasting inputs and data controls
Weather and calendar
Temperature, dew point, humidity, wind, pressure, hour, weekday, weekend, and Indian holidays
Demand history
5-minute, 1-hour, 1-day, and 1-week lags plus the rolling mean for the prior hour
Data quality watch
540 missing wind-direction values were forward-filled. 1,316 gaps exceeded five minutes.
The five-minute forecast combines weather, calendar context, and recent demand. Production monitoring must handle missing intervals before forecasts reach operations.
Notes: Feature inventory and data-quality observations are taken from the supplied notebook. The notebook forward-fills wind direction and reports timestamp intervals that are longer than the expected five-minute cadence.

## Slide 5: ML project coordination plan
Workstream | Current evidence | Decision / owner | Next checkpoint | Status
Data pipeline | 393,440 records, 2021–2024 | Confirm gap fallback rule | Before operational pilot | Needs decision
Feature pipeline | Weather, calendar, lag features | Version feature schema | Before retraining | In progress
Model selection | Linear regression leads validation | Approve baseline and model | Model review | Ready
Validation | 2024 MAE 24.59 MW; R² 0.9991 | Set error thresholds | Pilot readiness review | In progress
Operations | Five-minute forecast cadence | Define alert and rollback owner | Production handoff | Needs decision
Notes: Coordination plan translates the notebook evidence into decisions needed for an operational pilot. Statuses describe the work implied by the notebook and are planning prompts, not reported project facts.

## Slide 6: Decision for the next review
Approve the linear model for a monitored pilot
Set the missing-interval fallback and alert ownership
Notes: Decision request based on the supplied project notebook: move the selected linear model toward a monitored pilot only after the team assigns a fallback for missing timestamp intervals and operations ownership.